# Settings to transmit 8-channel sound via SRT
## Add Input -> Camera, all 8 embedded chanels in the SDI signal
Make sure that Audio Enabled and EmbeddAllChannels are selected.
Then divide the individual tracks into the MABC group.. Remember, each group (Master, A-F) has 2 channels each.
This is done under Input Settings, General, Audio Settings
## Channel Matrix
The individual SDI audio-tracks (numbers at the top of the matrix 1-8) are distributed to the groups MABC. For listening via headphones (Headphones L/R) all tracks can remain selected, this can still be changed, but is not relevant for the sound output.
## Output mixer
In the output mixer the individual audio tracks must be switched on.
## Receiver PC
The SRT input on the receiver side must have the same audio distribution settings as the SDI input from the transmitter PC,
AND also switch on all 4 groups of sound channels at the output mixer again.

## Settings OUTPUT
Make the following settings in the output settings for External1 (Output1).
Click on the gear wheel (in our example the one next to NDI OFF/Output1) and set the audio tracks MABC on Output1.
ATTENTION: For the SDI Out (External 1 & 2) only 8 tones are supported.
With the External OUT Settings (gear wheel in the footer next to the External button) also set the audio assignment MABC.